Protection and error handling
 
The IMS T9000 extends the error handling of earlier transputers to allow
error conditions to be easily trapped and handled in software. It can run
code in a protected mode where all memory accesses are checked and certain,
privileged, instructions cannot be executed.
 
--------------------------------------------------------------------------

Error handling
 
The first transputers have only a global mechanism for trapping errors;
stopping the entire processor when an error is detected. The IMS T9000
extends this to allow a trap handler to be associated with a process to
provide more localised error handling. When an error occurs, control is
transferred to the trap handler with information about the nature of the
error and where it occurred.
 
The action of a trap handler will, in general, be dependent on the language
or operating system being used and will be invisible to the applications
programmer. Some languages may include support for user written error
handlers. After taking the appropriate action, for example to report or
correct the error, the trap handler can return control to the process which
caused the error which can then continue execution. Each process can have
its own trap handler, or one trap handler can be shared by several (or all)
of the processes on the transputer.
 
To maintain compatibility with earlier transputers, the IMS T9000 can also
run processes in a global error mode where the behaviour on error is
identical to the IMS T805. These two types of processes are known as
L-processes and G-processes (for Local and Global error handling)
respectively. Both L- and G-processes can be run in parallel, the processor
dynamically switching modes as it switches between processes. This allows
code compiled for the IMS T805 (which will always be in global error mode)