Support for multiprocessing
 
The requirement for processing performance in embedded systems is
continuously increasing as control algorithms become more sophisticated and
as systems become more complex. In the long term, the only solution to
these ever increasing demands for performance is the use of multiple
processors to perform parallel processing.
 
Transputers are the only microprocessors specifically designed to  tackle
the problems of building multiprocessor systems.  There are advantages other
than just performance to using multiple transputers in a system; it allows
scalable systems to be built, where more processors can be added as demand
increases, or to provide the optimum balance of price versus performance.
The communications facilities of the transputer family can also be used to
build distributed systems where, for example, the processors are located
near the equipment or components they control and use links to communicate
with other processors in the system. In addition, transputers can be used
to build high reliability, fault tolerant systems.
 
Fast interrupt response and process switch
------------------------------------------
 
In most embedded applications, there is a need for fast real time  response
(both to external interrupts and for context switching in multitasking
systems). The design of the IMS T9000 processor exploits the presence of
the two on-chip caches by having only a small number of registers in the
CPU. This means that there is little state to be saved when an interrupt or
task switch occurs, so these operations are extremely fast. These types of
operations are very efficient on the transputer because of the hardware
scheduler.
 
The register stacks are duplicated so that, when a process running  on the
IMS T9000 is interrupted, the contents of the stacks do not need to be
written to memory. This results in a sub-microsecond interrupt response.
Furthermore, the duplication of the register stacks enables floating-point
arithmetic to be used in an interrupt routine without any performance
penalty.
 
-----------------------------------------------------------------
The transputer model of concurrency
 
The model of concurrency and communication implemented by the transputer
hardware is based on the ideas of communicating sequential processes. All
the features for creating processes and communicating between them are
accessible from any high level language for the transputer and are
implemented directly by the occam programming language [2].
 
Processes and channels
----------------------
 
Each process can be regarded as a black box with internal state, which  can
communicate with other processes using communication channels. Each channel
is a point to point connection between two processes. One process always
inputs from the channel and the other always outputs to it. Communication
is synchronised: the first process ready to communicate waits until the
second is also ready, then the data is copied from the outputting process
to the inputting process and both processes continue.
 
Each process starts, performs a number of actions and then terminates.  An
action may be a set of sequential processes performed one after another, as
in a conventional programming language, or a set of parallel processes to
be performed at the same time as one another. Since a process is itself
composed of processes, some of which may be executed in parallel, a process
may contain any amount of internal concurrency, and this may change with
time as processes start and terminate. Ultimately, all processes are
constructed from three primitive processes: assignment; input and output.
 
Program structure
-----------------
 
Figure 5.1 shows an example of a system constructed from three
communicating processes. In this case there are separate processes to
handle the external hardware (the screen and keyboard) and to execute the
main, application, process. This is a modular design - only the hardware
handling processes have to be changed if the software is moved to a new
environment, the same interface (the data sent and received on channels or
`protocol') can be presented to the application process. The keyboard
handler can be interrupt driven, only being scheduled when a character is
typed, the interrupts appearing as communications. The input and output
processes can provide buffering and other filtering of the data, all of
which is invisible to the main application process, which could even be
placed on a separate processor. This use of separate processors need not
just be for performance reasons but might be done, for instance, if there
are a large number of peripheral devices which could be better handled by a